Геоинформатика

Напряженно-деформированное состояние земной коры о. Сахалин 
c учетом воздействия вертикальных деформаций, вызванных эффектом гидроизостазии

Реферат. В работе предпринята попытка ответить на вопрос о роли вклада эффекта гидроизостазии в напряженно-деформированное состояние земной коры о. Сахалин. Оценка вклада гидроизостазии выполнялась моделированием методом конечных элементов. Сетка-меш для расчета была построена с использованием реальных поверхностей границы Мохо и топографии о. Сахалин с прилегающими шельфовыми участками. При расчете учитывалась Центрально-Сахалинская разломная зона. Моделировались латеральные деформации с вовлечением вертикальных деформаций. Сравнение результатов моделирования напряженно-деформированного состояния с учетом только латеральных деформаций и с вовлечением вертикальных деформаций со всей очевидностью демонстрирует значимость эффекта гидроизостазии в характере напряженно-деформированного состояния земной коры района о. Сахалин.

Stress-strain state of the earth's crust on Sakhalin Island, taking into account the impact of vertical deformations caused by the effect of hydroisostasis

Abstract. In this paper, an attempt is made to answer the question about the role of the contribution of the hydroisostasy effect to the stress-strain state of the Earth's crust on the island Sakhalin. The assessment of the contribution of hydroisostasis was carried out by modeling by the finite element method. The mesh for the calculation was built using real surfaces of the Moho boundary and the topography of Sakhalin Island with adjacent shelf areas. The calculation took into account the Central Sakhalin fault zone. Simulated lateral deformations involving vertical deformations. Comparison of the results of the stress-strain state only as a result of lateral deformations and with the involvement of vertical deformations clearly demonstrates the significance of the hydroisostasy effect on the nature of the stress-strain state of the earth's crust in the Sakhalin region.